## Slide 1: GPS-R Winds/SoOp Winds
HS-3 Science Team Meeting
NASA Research Park, Moffett Field, CA
James L Garrison Purdue University
Stephen J Katzberg, SCSU/NASA
Robert Holloway, ITT-Exelis
George Ganoe, NASA Langey

## Slide 2: Signals of Opportunity (SoOps)
Digital satellite signals re-used for sensing winds
First demonstrations used GNSS (GPS) signals
Recent works show techniques can be extended to most all communication satellites
Two instruments proposed for payloads of opportunity:
  2013: GPS-DMR (NASA Langley – Extensive flight heritage)
  2014: XM-Radio SoOp (Purdue/ITT – Flight prototype in development)

## Slide 3: Ocean Roughness/Wind Speed
Receiver
glistening zone
glistening zone
Fundamental Physics:
Rougher surface = larger distribution in path delays

## Slide 4: Ocean Roughness/Wind Speed
NOAA Hurricane Hunters
NASA P-3, N. Atlantic
March 2009
Wind Speed
[S. Katzberg, SCSU]
[Garrison, et al]

## Slide 5: NASA Langley GPS-DMR
Power: 13 W
Size (cm): 23 x 13 x 17
Box weight: 2.800 Kg
Antenna (1 piece): 0.115 Kg
Typical weight: 3.030 Kg
Stack weight: 0.630 Kg
Antenna (1 piece): 0.115 Kg
Min weight: 0.860 Kg
Langley Research Center – Research and Technology

## Slide 6: What about other signals ?
Approximately 400 communication satellites in GEO
High-powered (~30 dB above GNSS) signals
Allocations in most bands used for remote sensing:
  L,S, C, Ku/Ka
Designed for data transmission – Not ranging!
Assumption: Compression & Encryption are very efficient at filling available spectrum
  Data is nearly random
  Direct signal can be used as reference

## Slide 7
SoOp Reflectometry Instruments
GPS Delay-Mapping
Receiver (DMR)
GPS Reflection
Antenna
Reflected GPS/XM
Antenna
XM Radio
Signal Recorder
Reflected GPS
Antenna

## Slide 8: NOAA SoOp Instrument
ANTENNA
AMPLIFIER
3U
PC-104
USRP
BACK VIEW
FRONT VIEW
19”
Notes: Size

## Slide 9: XM Radio (S-band) Reflectometry
Wind Speed Dependence
Comparison with Model

## Slide 10: Simulated Wind Speed Retrievals

## Slide 11: HS-3 SoOp Receiver: FPGA-Based SoOp Processor
FPGA-Based real-time correlators
23x18x8 cm
<7 W
<1 Kg.
Configured for XM radio (S-band)
interchangable front-ends
ITT-Exelis IRAD funding

## Slide 12: HS-3 SoOp Receiver: Combined GPS/XM Antenna

## Slide 13: Status
GPS-DMR: Receiver ready to go – seeking integration funds
HS-3 SoOp Receiver
  FPGA working with stored digital data
  June 2013 – Planned demo with live sky signals
  Summer 2013 – test flight on light A/C
  Dec. 2013 – Flight unit delivery.
  Seeking integration funds

## Slide 14
Backups and Extras

## Slide 15: Advantages of SoOp for UAVs
Strong, coherent signal provide for free, hence:
  Passive
  Very small antennas (usually low-gain patches)
  Very small, low power receiver
  Resistance to RFI
Use of non-protected frequencies
Some measurements require little power calibration
  Basic observation: signal correlation function, not scattering coefficient
  Direct signal available for relative power measurement

## Slide 16: Hi-Winds 2009 Experiment
Integration at Wallops Is., VA
NASA Langley DMR
GNSS-R Antenna

## Slide 17: Collaborators
ITT-Exelis: SoOp Receiver development (IR&D)
NASA Langley/South Carolina State: GPS DMR
Flight campaigns: JPL (2009), NRL (2011)
NOAA: Hurricane hunter flights
NCAR: HIAPER-GISMOS Receiver
Purdue Dept. Earth & Atmospheric Science, School of Agricultural and Biological Eng.

## Slide 18: Hi-Winds 2009 Experiment

## Slide 19: NASA Langley GPS-DMR
Description
Weight: 0.860 – 3.00 Kg
Power consumption: 13 watts
Dimensions: 23 x 13 x 17 cm
Antenna diameter: 10 cm
Potential applications
Soil moisture mapping
Altimetry
Freeze/thaw monitoring
Points of contact
Dr. Stephen J. Katzberg, PI
Phone: (803) 516-6068
Email: Stephen.J.Katzberg@nasa.gov
George G. Ganoe
Phone: (757) 864-3707
Email: michael.s.grant@nasa.gov
http://dragon.larc.nasa.gov/gps

## Slide 20: GPS technique is UAV friendly
Langley Research Center – Research and Technology