## Slide 1
Instrumented Balloon Launches for ATTREX
Dale Hurst, Emrys Hall, Allen Jordan
Global Monitoring Division, NOAA Earth System Research Laboratory
and CIRES, University of Colorado, Boulder
Boulder Balloon Soundings … still going strong after 33 years!

## Slide 2
Ozonesonde
Radiosonde
NOAA FPH
Air
Intake Tubes
Payload Weight: 2.0 kg (4.4 lb)
Payload Size: 15” x 12” x 8”
Instrument Payload

## Slide 3
Payload Measurements
Primary Data Uncertainty
Instrument Measurement Product (Stratosphere)
NOAA FPH TFP H2O VMR <±10% (±0.5 ppmv)
(custom)
P
P
Ozonesonde PO3 O3 VMR <±5% (±0.3 ppmv )
(DMT)
Radiosonde T <±0.5° C
(Intermet) P <±0.5 hPa
403 MHz RH NA > 12 km
GPS payload location, horizontal winds

## Slide 4
Balloon Flight Profile
Ascent Rate
+5 m/s
(1000 ft/s)
Valve opens
Descent Rate
-5 m/s
~ 70 minutes
~ 90 minutes

## Slide 6
Ideally …
Coordination with GH flights
• 1 balloon launch per GH flight
• 4-6 flights anticipated (4 week window)
• Close spatiotemporal coincidence with GH
• Requires launch timing and trajectory to be
coordinated with GH flight plan

## Slide 7
Balloon Trajectory Prediction (2D)

## Slide 8
Balloon Trajectory Prediction (3D)

## Slide 9
Potential Launch Sites
Andersen
AFB
NWS
Facility

## Slide 10
Ballooning over the Rockies

## Slide 11
FPH Measurement Technique
Stable Frost Layer =
equilibrium between frost layer and water vapor in air flow
PH2O = f(TFP) Clausius-Clapeyron equation (Psat over ice)
H2O VMR = PH2O / (Pair – PH2O)
Calibrated
NIST scale
PID Temp Controller